## Slide 1: Uncertainty in Mechanics of Materials

## Slide 2: Outline
Uncertainty in mechanics of materials
Why consider uncertainty
Basics of uncertainty
Uncertainty analysis in mechanics of materials
Examples
Applications
2

## Slide 3: Uncertainty in Mechanics of Materials
Example
Given: P=100 kN, Q=40 kN, L1 =0.5 m, L2 =1 m, b=0.1 m, h=0.2 m
Find: The maximum normal stress Smax
Solution: Smax=135 MPa
In reality, all the input variables are random. So is Smax.
Smax will fluctuate around 135 MPa.
3

## Slide 4: Where Does Uncertainty Come From?
Manufacturing impression
  Dimensions of a mechanism
  Material properties
Environment
  Loading
  Temperature
  Different users
4

## Slide 5: Why Consider Uncertainty?
We know the true solution.
We know the effect of uncertainty.
We can make more reliable decisions.
  If we know uncertainties in the above beam problem, we can design a better beam so that its likelihood of failure will be low and its performance will be not affected by the uncertainties.
5

## Slide 6: How Do We Model Uncertainty?
6
For the beam problem, measure the force P (or X) 10 times,
we get
How do we use the samples?
Average

## Slide 7: How Do We Measure the Dispersion?
7
We could use and ,
But .
To avoid 0, we use ; To have the same unit as ,
we use .
We actually use Standard deviation: .
Now we have , for . (Use Excel)

## Slide 8: More about Standard Deviation (std)
It indicates how data spread around the mean.
It is always non-negative.
High std means
  High dispersion
  High uncertainty
  High risk
8

## Slide 9: Probability Distribution
With more samples (eg. The number of samples=1000), we can draw a histogram of .
9
If y-axis is frequency and the number of samples is infinity, we get a probability density function (PDF) .
The probability of .

## Slide 10: Normal Distribution
is called cumulative distribution function (CDF)
10

## Slide 11
Use Excel
  NORMDIST(x,mean,std,cumulative)
  cumulative=true
11

## Slide 12: More Than One Random Variables
are independent
are constants.
Then
12

## Slide 13: Example
13
Two random forces and are exerted on a cantilevered beam. The dimensions are and The allowable normal stress Sa of the beam is also a random variable with MPa. P, Q, and Sa are independent. Determine the probability of failure of the beam.

## Slide 14: Moment Diagram
14

## Slide 15
The maximum normal stress is given by
The probability of failure is .
Let .
Then .
pf is written as . Since normal random
variables P, Q and Sa are independent, Y also follows a
normal distribution, .
15

## Slide 16
Thus
a
Therefore,
The probability of failure of the beam is .
16

## Slide 17: Conclusions
Uncertainty is ubiquitous in engineering, including applications of mechanics of materials.
Uncertainty is usually modeled by probability theory.
Considering uncertainty promotes high reliability, robustness, and safety.

## Slide 18: Assignment
On Blackboard.
More readings: http://web.mst.edu/~dux/repository/ce110/ce110.html
18