## Slide 1: Robust Design and Reliability-Based Design
ME 4761 Engineering Design 2015 Spring Xiaoping Du

## Slide 2: Outline
Definition of robustness
Introductory examples
Statistics
How to achieve robustness
Examples
Related methodology: reliability-based design
Conclusions

## Slide 3: Robust Design
If a design can work properly even when subjected to variation, it is robust.
Variation (uncertainty) may be introduced by
  manufacturing processes
  environment
  parts from outside suppliers
  end user

## Slide 4: Robustness
The robustness of a product is the ability that its performances are not affected by the uncertain inputs or environment conditions (noises).
Robustness is insensitivity to uncertainty.
A robust product can work under large uncertainties.

## Slide 5: Variation (Uncertainty)
Piece-to-piece variation
Customer usage and duty cycle
Human errors
Model inaccuracy
Uncertainty
Present state of knowledge
Complete ignorance
Knowledge
Complete knowledge

## Slide 6: An Example: Cantilever Beam
h1
h2
b2
b1
l2
l1
P
A
A
A - A
B
C
The maximum stress
The material strength
Factor of safety
Reality: everything is uncertain
Load: P=(2001.4, 1531.3, 2534.6, ….) kN
Yield strength: Sy=(120.5, 101.3, 131.2, 170.9,…) MPa
Dimension: h1= 1000.01 mm
Dimension: b1= 500.01 mm, ….

## Slide 7: Principle of Robust Design
Minimize the effect of uncertainty (variation) without eliminating the cause of uncertainty.
How?
By changing design variables to make the performance not sensitive to uncertainty.

## Slide 8: Example: Tile Manufacturing
Output: Tile dimensions
Problem: Large variability in dimensions
Uncertainty source: Huge variation in temperature
Possible solutions
  Screening
  Redesign the kiln
  Too expensive
Robust design solution
  Do not control the temperature
  Change design variables: increasing the lime content of the clay from 1% to 5%
  Inexpensive
Phadke: Quality Engineering Using Robust Design, 1989

## Slide 9: Benefits of Robust Design
Product performance insensitive to material variation –> use of low grade material and components
Product performance insensitive to manufacturing variation -> reduced labor and manufacturing cost
Product performance insensitive to the variation in operating environment -> higher reliability and lower operation cost

## Slide 10: How Do We Quantify Uncertainty?
Support we have 100 measurements for
(99.99, 100.08,…,100.05) mm
Average
Dispersion
Histogram
Probability density (distribution)

## Slide 11: Probability Distribution
Mean – average
Standard deviation (std) – dispersion around the average or amount of variation
Two designs with two performance variables
,
Designs 1 and 2 have the same average performance
The variation of Design 1 is smaller
Design 1 is more robust
Design 1
,
Design 2
,

## Slide 12: TV Example
In 1970s, Americans showed a preference for television sets made by Sony-Japan over those made by Sony-USA.
The color density was a major performance.
  Target ± tolerance = m ± 5.
Sony-Japan sets: 0.3% defective sets (outside the tolerance limits)
Sony-USA sets: virtually NO sets outside the tolerance limits.
Why?
Phadke: Quality Engineering Using Robust Design, 1989

## Slide 13: TV Example
Sony-USA: Uniform distribution,
Sony-Japan: Normal distribution, , and most of the sets are grade A.
Phadke: Quality Engineering Using Robust Design, 1989

## Slide 14: How to Evaluate Robustness?
Traditional design
  m: target, : tolerance
  L(y): quality loss = 0 within the tolerance limits
Robust design
  Taguchi’s quality loss ($) , k: constant
  quality loss = 0 only at m
L(y)
m
m-
m+
y
L(y)
y
m
m-
m+

## Slide 15: Expected Quality Loss
  Expected (average) quality loss
  ]
  Minimizing will bring the average performance to the target and reducing variation simultaneously.
Initial design
Final design

## Slide 16: Robust Design
Increasing robustness
Decreasing variation
Increasing average performance

## Slide 17: Other Types of Quality Loss
What we’ve discussed is the “nominal-the-better” type
The “smaller-the-better” type
  cost, stress, energy consumption
The “larger-the-better” type
  life, reliability, strength, efficiency
y
L(y)
0
y
L(y)
0

## Slide 18: How to Select Design Variables to Achieve Robustness?
Performance
Design variables
are independent

## Slide 19: Parameter Design
Average performance
Taylor expansion series
)
Std
  Change (not reduce ) to minimize
  ]
Taylor expansion
X
Y
0
Sensitivity

## Slide 20: More about Sensitivity
Input x
Output y
Sensitive
Insensitive
(robust)

## Slide 21: Example: Robust Mechanism Synthesis
Requirements:
  mm when 
  mm when 
Uncertainties in a, b, and e
  mm, ,
Design variables
,
a
b
e
A
N
N
C
B


## Slide 22: Results
Method | Deterministic Design | Robust Design
(mm) | 119.6 | 136.6
(mm) | 241.3 | 216.8
(mm) | 45.0 | 0.0
() (mm) | 350 | 350
() (mm) | 250 | 250
() (mm) | 2.9 | 2.8
() (mm) | 3.5 | 3.1
Method | Deterministic Design | Robust Design
 | 119.6 | 136.6
 | 241.3 | 216.8
 | 45.0 | 0.0
 | 350 | 350
 | 250 | 250
 | 2.9 | 2.8
 | 3.5 | 3.1
  Minimize ]
Transmission angle > 45

## Slide 23: Example 2 - Piston Engine Robust Design
 | Baseline | Optimal
Mean of f | 54.5 dB | 54.2 dB
Std of f | 2.04 dB | 0.76 dB
Prob | 0.65 | 0.99
Liner
f – Slap noise
G - Friction

## Slide 24: Other Method Operating Window Methods
Developed by Xerox.
The operating window is the set of conditions under which the system operates without failure.
A wider window can accommodate larger uncertainties.
Robustness is achieved by making the operating window larger.

## Slide 25: Related Issue: Reliability (R)
The ability of a product performing its intended function
probability of no failure
x1
Failure region
Safe region
Boundary
x2
Deterministic optimal point

## Slide 26: Reliability vs. Robustness
Everyday fluctuations around the mean – deterioration, degradation, quality loss
Extreme events at tails – failure, catastrophe
Reliability issue
  Motherboard failure
  Broken hard disk
Robustness issue
  Overheating
  Noise

## Slide 27: How to Design for Reliability?
Conceptual design
  Failure mode and effects analysis (FMEA) (IDE 20 & ME 161)
Parameter design
  Reliability-based design
x2
x1
Failure Region
Safe Region
x2
x1
Failure Region
Safe Region

## Slide 28: Software Tools
iSIGHT
MSC – Robust Design
  Robust Design for Whirlpool Products
  http://www.mscsoftware.com/success/details.cfm?Q=285&sid=282
Ansys – Monte Carlo Simulation
ADAMS – Design of Experiments

## Slide 29: Conclusions
Robust design -> insensitivity to uncertainties
  Insensitive to material variations-> use of low grade materials and components -> low material cost
  Insensitive to manufacturing variations -> no tightened tolerances -> low manufacturing and labor cost
  Insensitive to variations in operation environment -> low operation cost
Robust design -> increased performance, quality, and reliability at reduced cost
Robustness and reliability can be built into products during early stages of design.

## Slide 30: More Information
Visit the website of Engineering Uncertainty Repository at http://www.mst.edu/~dux/repository.
Contact me
  Toomey Hall 272
  dux@mst.edu